Conditions:
Matrix is configured for two RGB chains, except where mentioned otherwise.

Firmware is configured with the following settings:
- Number of steps is 16.
- Number of columns is 8.
- Number of scans is 4.
- Baud rate 7.8MBaud.
- PWM Algorithm using BUS8.
- Decoder Multiplexer using BUS8.
- UART Node using Serial Protocol.
- UART flow control enabled.
Chapter 1: Logic
Section 1: Verify PMP PIO:
Case 1: Verify clock is 8.33MHz.
Case 2: Verify clock wave form is square with 8 loads.
Case 3: Verify clock remains constantly on.
Case 4: Verify all PWM periods are present plus null period.
Case 5: Verify LAT is one clock pulse.

Section 2: Verify Multiplexer PIO
Case 1: Verify refresh is at least 3kHz.
Case 2: Verify proper progress from A, B and C of decoder.
Case 3: Verify all 8 scans are present.
Case 4: Multiplexing is only started after null period.
Case 5: Verify OE is high only for blank time.

Section 3: Verify Ghost PIO
Case 1: Verify LEDs discharge (turn on) within one GCLK period.
Case 2: Verify LEDs charge (turn off) within one GCLK period.
Case 3: Verify blank time is 10uS.
Case 4: Verify brightness is at least 60 percent.
Case 5: Verify PMOS capacitors charge and discharge within blank time.
Case 6: Verify multiplexing has completed within blank time.

Section 4: Multiplexer
Case 1: Verify frame transition is synced to FCLK.
Case 2: Verify frame transition is within on refresh.
Case 3: Verify frame transition is only at the top of a scan.
Case 4: Verify FCLK on time a quarter of the frame time.

Section 5: Interface
Case 1: Verify swap command acknowledged before FCLK.
Case 2: Frames are retained till another frames arrives.
Case 3: Verify flow control signals respond.

Chapter 2: Timing
Section 1: Verify BUS8
Case 1: All data pins are setup at least 5nS before clock edge.
Case 2: All data pins are held for at least 5nS after clock edge.
Case 3: Clock is stopped for LAT signal.
Case 4: Verify OE on or off time is never shorter than 200nS.
Case 5: LAT arrives after last data shift.
Case 6: LAT pin rises 20nS after clock period.
Case 7: LAT pin is held for 10nS.

Section 2: RP2040 processing
Case 1: Verify multiplexing is never slowed by frame swap or data operations.
Case 2: Verify data is consumed faster than data rate.
Case 3: Verify processing frame rate exceeds 240 FPS.
Chapter 3: Power
Section 1: Voltage
Case 1: Verify the voltage to the LED driver is 3.3V +/- 0.1V under max and min load.
Case 2: Verify the voltage to the LEDs is 5V +/- 0.01V under max and min load.

Section 2: Current
Case 1: Verify current response time is 10kHz or higher.
Case 2: Verify decoupling of LED drivers and LEDs.
Case 3: Verify RP2040 subsystem draws no more than 60mA.
Case 4: Verify LED drivers are accurate to +/- 3 percent between any channel.
Case 5: Verify a pixel of up to three colors draws no more than 30mA.

Section 3: Module
Case 1: Dedicated power conversion from 12V to 5V is available.
Case 2: Dedicated power conversion from 5V to 3.3V is available.

Chapter 4: EMI
Section 1: Interface
Case 1: Verify balanced differential signals.
Case 2: Galvanic isolation is used.

Section 2: Power
Case 1: Chokes are used on 12V line.
Case 2: Ground power is stable.

Chapter 5: Commands
Section 1: Data command
Section 2: Test command
Section 3: Power command
Section 4: Swap command
Section 5: Reboot command

Chapter 6: Protocol

Chapter 7: Node
Section 1: UART
Case 1: Verify flow control.
Case 2: Verify max baud.
Case 3: Verify start, stop, 8 bits, parity none.

Chapter 8: Watchdog

Chapter 9: Bootloader

Chapter 10: LED driver detection

Chapter 11: Thermal
Section 1: LED drivers
Section 2: Environment